## Slide 1: MASTER1 INTELLIGENCE ARTIFICIELLE ET INTERNET DES OBJETS
Internet of Things - IoT
Korota Arsène COULIBALY ENSAM de Casablanca, Maroc
Année universitaire 2024-2025

## Slide 2: Programme
Introduction to IoT
MQTT Protocol
IoT platform
Embedded system and end devices programmation

## Slide 3: Objectifs du programme
Objectif principal :
Être capable de concevoir un système IoT
Objectifs pédagogiques:
Décrire un système IoT;
Décrire les systèmes embarqués;
Comprendre les contraintes des systèmes embaqués vis-à-vis de l’IoT;
Choisir et mettre en place une plateforme IoT;
Décrire et choisir le protocole de communication sans fil adapté pour son application IoT

## Slide 4: Introduction to Internet of Things
Le problème de la collecte des récipients en verre en milieu urbain : un spectacle pas si inhabituel …
La solution : assurer la collecte des récipients en verre AVANT que la poubelle ne soit pleine.
Les moyens : équiper la poubelle
d’un capteur de niveau de remplissage qui alerte automatiquement le centre de collecte de ce qu’elle est presque pleine, et que donc, il faut la vider.
-> Internet des Objets

## Slide 5: Introduction to Internet of Things
Les principales caractéristiques de l’IoT
Une couverture radio le plus large possible
Une interopérabilité avec les réseaux câblés, sans fil et cellulaires existants
Une transmission radio essentiellement unidirectionnelle (de l’objet vers la passerelle)
Une technologie radio faible consommation
Une transmission de données de faible volume, à bas débit et discontinue

## Slide 6: Introduction to Internet of Things
Optimisation de la collecte des récipients en verre
Tous les jours, avant que ne débute la collecte, les poubelles (1) transmettent leur taux de remplissage (de 0 à 100%) à une passerelle (2).
Les informations collectées sont ensuite transmises à un serveur et mises à disposition sur le « cloud » (3).
L’opérateur chargé de la collecte des poubelles récupère les informations (4) et optimise sa tournée (5) de façon à ne collecter que les poubelles jugées suffisamment pleines.

## Slide 7: Introduction to Internet of Things
L’IoT est un système dans lequel des objets appelés Nœuds (Node) ou End Devices collectent des données et les injectent directement sur le réseau internet ou via une passerelle (gateway). Ces objets sont capables de s’échanger des données.

## Slide 8: Introduction to Internet of Things

## Slide 9: Introduction to Internet of Things

## Slide 10: MQTT - Publisher - Broker - Subscriber
MQTT = Message Queuing Telemetry Transport
End device (ESP32 node)
IoT Platform
MQTT

## Slide 11: MQTT - Publisher - Broker - Subscriber
BROKER

## Slide 12: MQTT - Publisher - Broker – Subscriber
BROKER
T° sensor
H° sensor

## Slide 13: MQTT - Publisher - Broker - Subscriber
BROKER
T° sensor
TOPIC Temperature
TOPIC Humidity
H° sensor
Publisher
Publisher
Heating system
Subscriber
Drying system
Subscriber

## Slide 14: MQTT - Publisher - Broker - Subscriber
House
Room
Living-room
T°
sensor
H°
sensor
Noise sensor
T°
sensor
H°
sensor
Noise sensor
I’m looking for the temperature in the bedroom of the house:
TOPIC  House/Room/T°sensor
I’m looking for the temperature in the living-room of the house:
TOPIC  House/Living-room/T°sensor
I’m looking for all the sensors in the house:
TOPIC  House/# or #
I’m looking for all temperatures in the house:
TOPIC  House/+/T°sensor

## Slide 15: MQTT - Publisher - Broker - Subscriber
MQTT characteristics
Publisher and subscriber don't know each other.
Infinite number of topics.
Topics are created by the publishers.
Authentication procedure to publish or subscribe to the broker.
…

## Slide 16: MQTT – Demonstration with a public broker
Publisher
Subscriber
Our demonstration

## Slide 17: MQTT – Demonstration with a public broker
Publisher
Subscriber
Our demonstration
We could set up our own
or
We can use a public broker
A famous one:
Another example:
MQTT
client
E.g.:
Client controlled by a Command Line Interface (CLI)
Client using Node-RED
Client with a standalone user interface

## Slide 18: MQTT – Demonstration with a public broker
Our demonstration
or
Publisher
Subscriber
Client configuration:
Server we want to connect to
The Login and password for the connection
The topic we want to target (for publisher). The topic we want to read (for subscriber)
The message to send to the specified topic (for publisher)

## Slide 19: MQTT – Demonstration with a public broker
Publisher
Subscriber
Our demonstration
First part of the demonstration
Publisher
Subscriber
Second part of the demonstration

## Slide 20: IoT Platform architectures
IoT platform

## Slide 21: IoT Platform architectures
IoT platform
IoT Platform solutions … There are plenty of them !
Our solutions:
Most of them are free & open-source
Can work both with uplink and downlink streams

## Slide 22: IoT Platform architectures
IoT platform
Web Server and UI
Data visualization
Data storage
HTTP
MQTT
Data collection and transfer
Example:
HTTP and MQTT connections, Graphical UI, etc.

## Slide 23: IoT Platform architectures
IoT platform
Web Server and UI
Data visualization
Data storage
Our solution :
To connect our IoT Platform to our End device
To store data
To create dashboards and customize our User Interface
HTTP
MQTT
Data collection and transfer

## Slide 24: IoT Platform architectures
IoT platform
To connect our IoT Platform to our End device
Our solution :
To store data
To create dashboards and customize our User Interface
MQTT broker
MING Stack
Mosquitto InfluxdB NodeRED Grafana

## Slide 25: IoT Platform architectures
IoT platform
To connect our IoT Platform to our End device
Another solution:
To store data
To create dashboards and customize our User Interface
ELK Stack
Elasticsearch Logstash Kibana

## Slide 26: IoT Platform architectures
IoT platform
Another way:
Use an IoT platform without creating one.
A professional service !
Not free
Good choice for a big project

## Slide 27: Our IoT platform solution
IoT platform
Our solution :
End-device
Gateway 1
LDR value
Potentiometer value
LEDs state

## Slide 28: Our IoT platform solution
Our solution :
MQTT (uplink)
MQTT (downlink)
NodeRED acts as a subscriber to get uplinks, and as a publisher to send downlinks.
End
device

## Slide 29: Our IoT platform solution
Our solution :
MQTT (uplink)
MQTT (downlink)
Data to save
Influxdb is a software installed separately.
NodeRED acts as a subscriber to get uplinks, and as a publisher to send downlinks.
End
device

## Slide 30: Our IoT platform solution
Our solution :
MQTT (uplink)
MQTT (downlink)
Data to save
Influxdb is a software installed separately.
Data to display
Grafana requests the data it needs for the creation of graphs, etc.
NodeRED acts as a subscriber to get uplinks, and as a publisher to send downlinks.
End
device

## Slide 31: Our IoT platform solution
Our solution :
MQTT (uplink)
MQTT (downlink)
Data to save
Data to display
How to install these services ?
With Docker !
Where can we set up this IoT platform ?
Anywhere !
In our case: Raspberry pi
End
device

## Slide 32: Our IoT platform solution
Our solution :
MQTT (uplink)
MQTT (downlink)
Data to save
Data to display
Public Server
Public Server
Public Server
Organization example:
Container talk to each other thanks to an IP address on a specific port.
End
device

## Slide 33: Our IoT platform solution
MQTT communication
NodeRED UI
Access Influxdb
Access Influxdb
Influxdb UI
Grafana UI
Our solution:
Everything is on the same public server
Port 1883
Port 1880
Port 8086
Port 8086
Port 8086
Port 3000
End
device

## Slide 34: Our IoT platform specifications
Let’s build our IoT Platform !
1 dashboard with Temperature, LDR value, potentiometter value, LEDs state
Our requirements:
Steps to achieve our goal:
Step 1 Build an MQTT subscriber on Node-RED to get the uplink data.
Step 2
Extract the exact value we want: the temperature LDR value, potar value, LEDs state. Send the extracted values to Influxdb.
Check our data are available on Influxdb.
Step 3
Tell Grafana how it can access the database. Create a request to get the values we need.

## Slide 35: Embedded systems
Embeddded system = Hardware part + Software part
electronic
User application

## Slide 36: Embedded systems – Hardware architecture
The embedded hardware is where the software (user application) will be embedded. It may be a microcontroller board or a CPU based board.
Microcontroller
MCU based board
DSP based board
FPGA based board

## Slide 37: Raspberry pi
Operating System
Raspberry pi OS
Ubuntu
Windows 10 Arm
Single board computer
Single board computer

## Slide 38: Raspberry pi

## Slide 39: Raspberry pi

## Slide 40: Raspberry pi

## Slide 41: Raspberry pi

## Slide 42: Raspberry pi

## Slide 43: Raspberry pi

## Slide 44: Raspberry pi

## Slide 45: Embedded systems – Hardware architecture
ESP boards: ESP32 & ESP8266
ESP32 and ESP8266 are series of MCU chips developed by Espressif.
Why ESP32 ?
Low cost : 150Dh
Low energy consumption
WiFi & Bluetooth
Two cores : Xtensa 32 bits
I/O interfaces : ADC DAC, SPI, I2C, UART, PWM
Supports Arduino programming language and MicroPython

## Slide 46: Embedded system – Hardware architecture
ESP boards: ESP32 & ESP8266

## Slide 47: Embedded system – Hardware architecture
ESP boards: ESP32 & ESP8266
How to program ESP boards ?
Espressif IDF (IoT Development Framework)
Arduino C/C++ with Arduino ESP core:
MicroPython
In this course we’ll used Arduino with PlatformIO

## Slide 48: Embedded system – Hardware architecture
ESP boards: ESP32 & ESP8266
Configuration of development environment
Download and install
Install PlatformIO extension in VS Code

## Slide 49: Embedded system – Hardware architecture
ESP boards: ESP32 & ESP8266
Configuration of development environment
1. Download and install Arduino sw
2. Install esp32 and esp8266 Arduino core
3. Add esp32 and esp8266 boards url in Arduino sw
ESP32 url : http://arduino.esp8266.com/stable/package_esp8266com_index.json
ESP8266 url: https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json
Copy two url and colle in :
File -> Preferences -> Additional boards manager urls